## Slide 1: How the Web Works
Layered Architecture

## Slide 2: Layered Architecture
Provides a means for dissimilar hardware or software to communicate
Provides a level of abstraction from layer to another
Relies on standards and protocols
Examples:
  Should the computer hardware you use determine how your web browser behaves?
  Should the switch you connect to care what web browser you are using?
  Should the web server care what web browser you are using?
Two prominent models
  Internet Protocol Suite (IP) Model
  Open Systems Interconnection (OSI) Model

## Slide 3: Internet Protocol Suite (IP) Model
Four Layers
  Application focuses on the process/services
    HTTP, SSH, FTP, mail, DNS, etc.
  Transport focuses on the host-to-host communication
    UDP (connection-less) vs. TCP (connection-oriented)
  Internet focuses on network addressing and routing
    IP Address (IPv4 vs. IPv6)
  Link focuses on hardware and network topology
    MAC Address
Application
Transport
Internet
Link

## Slide 4: Open Systems Interconnection (OSI) model
Seven layers
  Application - overarching process/service
  Presentation - data formatting and data translation
  Session – setup, manages connections
  Transport - functional and procedural means of transferring variable-length data sequences
  Network - transfer packets between nodes
  Data Link – corrects/manages errors
  Physical - unstructured raw data
Application
Transport
Internet
Link

## Slide 5: Topology
Application
Transport
Internet
Link
Ethernet
Application
Transport
Internet
Link
Ethernet
Layered networks
process-to-process
host-to-host

## Slide 6: Relevant Application Layer protocols
HTTP - Hypertext Transfer Protocol
SSH - Secure Shell
FTP - File Transfer Protocol
POP/IMAP/SMTP - Email related protocols (out of scope for us)
DNS - Domain Name System